## Slide 1: Unit – 1 RETAINING WALLS
Retaining walls
Retaining walls are structure used to retain soil, rock or other materials in a vertical condition. Hence they provide a lateral
support to vertical slopes of soils that would
otherwise collapse into a more natural shapes.
Backfills
The material retained are supported by retaining may
wall inclined or Horizontal.
The back fill laying above the Horizontal plane
top of at the elevation of the wall is called surcharge.
Gravity Retaining wall

## Slide 2
Retaining walls

## Slide 3: Cantilever retaining wall with shear key

## Slide 4
Classification of Retaining walls
Gravity wall-Masonry or Plain concrete
Cantilever retaining wall-RCC
(Inverted T and L)
Counterfort retaining wall-RCC
Buttress wall-RCC

## Slide 5: Classification of Retaining walls
Counterfort
Gravity RW
Gravity RW
T-Shaped RW
L-Shaped RW
Backfill
Backfill
Counterfort RW
Buttress
Backfill
Buttress RW

## Slide 6
Earth pressure is the pressure exerted by the retaining material on the retaining wall. This pressure tends to deflect the wall outward.
Types of earth pressure :
Active earth pressure or earth pressure (Pa) and
Passive earth pressure (Pp).
Active earth pressure tends to deflect the wall away from the backfill.
Pa
GL
Variation of Earth pressure
Earth Pressure (P)

## Slide 7: Earth pressure depends on type of backfill, the height of wall and the soil conditions
Soil conditions: The different soil conditions are
Dry leveled back fill
Moist leveled backfill
Submerged leveled backfill
Leveled backfill with uniform surcharge
Backfill with sloping surface

## Slide 8
Maximum pressure at any height, p=kah
Total pressure at any height from top, pa=1/2[kah]h = [kah2]/2
Bending moment at any height
M=paxh/3= [kah3]/6
 Total pressure, Pa= [kaH2]/2
Total Bending moment at bottom,
M = [kaH3]/6
Pa
H
h
kaH
M
Analysis for dry back fills

## Slide 9
Where, ka= Coefficient of active earth pressure
= (1-sin)/(1+sin)=tan2
= 1/kp, coefficient of passive earth pressure
= Angle of internal friction or angle of repose
=Unit weigh or density of backfill
If = 30, ka=1/3 and kp=3. Thus ka is 9 times kp

## Slide 10
pa= ka H at the bottom and is parallel to inclined surface of backfill
ka=
Where =Angle of surcharge
Total pressure at bottom
=Pa= ka H2/2
Backfill with sloping surface

## Slide 11
When H exceeds about 6m,
Stem and heel thickness is more
More bending and more steel
Cantilever-T type-Uneconomical
Counterforts-Trapezoidal section
1.5m -3m c/c
Counterfort Retaining wall
CRW
CF
Base Slab
Stem

## Slide 12: Parts of CRW
Same as that of Cantilever Retaining wall Plus Counterfort
Stem
Toe
Heel
Base slab
Counterforts
Cross section
Plan

## Slide 13
The stem acts as a continuous slab
Soil pressure acts as the load on the slab.
Earth pressure varies linearly over the height
The slab deflects away from the earth face between the counterforts
The bending moment in the stem is maximum at the base and reduces towards top.
But the thickness of the wall is kept constant and only the area of steel is reduced.
Design of Stem
BF
p=Kaγh

## Slide 14: Design of Toe Slab
The base width=b =0.6 H to 0.7 H
The projection=1/3 to 1/4 of base width.
The toe slab is subjected to an upward soil reaction and is designed as a cantilever slab fixed at the front face of the stem.
Reinforcement is provided on earth face along the length of the toe slab.
In case the toe slab projection is large i.e. > b/3, front counterforts are provided above the toe slab and the slab is designed as a continuous horizontal slab spanning between the front counterforts.
b
H

## Slide 15
The heel slab is designed as a continuous slab spanning over the counterforts and is subjected to downward forces due to weight of soil plus self weight of slab and an upward force due to soil reaction.
Maximum +ve B.M= pl2/16
(mid-way between counterforts)
And
Maximum -ve B.M= pl2/12
(occurring at counterforts)
Design of Heel Slab
BF

## Slide 16: Design of Counterforts
The counterforts are subjected to outward reaction from the stem.
This produces tension along the outer sloping face of the counterforts.
The inner face supporting the stem is in compression. Thus counterforts are designed as a T-beam of varying depth.
The main steel provided along the sloping face shall be anchored properly at both ends.
The depth of the counterfort is measured perpendicular to the sloping side.
T
C
d

## Slide 17: Behaviour of Counterfort RW
-M
-M
TOE
COUNTERFORT
+M
+M
STEM
HEEL SLAB
Important points
Loads on Wall
Deflected shape
Nature of BMs
Position of steel
Counterfort details

## Slide 18
Design a cantilever retaining wall (T type) to retain earth for a height of 4m. The backfill is horizontal. The density of soil is 18kN/m3. Safe bearing capacity of soil is 200 kN/m2. Take the co-efficient of friction between concrete and soil as 0.6. The angle of repose is 30°. Use M20 concrete and Fe415 steel.
Solution
Data: h' = 4m, SBC= 200 kN/m2, = 18 kN/m3, μ=0.6, φ=30°
Cantilever RW design

## Slide 19: Depth of foundation
To fix the height of retaining wall [H]
H= h' +Df
Depth of foundation
Df =
= 1.23m say 1.2m ,
Therefore H= 5.2m
H
200
b
Df
h1
h

## Slide 20: Proportioning of wall
Thickness of base slab=(1/10 to1/14)H
0.52m to 0.43m, say 450 mm
Width of base slab=b = (0.5 to 0.6) H
2.6m to 3.12m say 3m
Toe projection= pj= (1/3 to ¼)H
1m to 0.75m say 0.75m
Provide 450 mm thickness for the stem at the base and 200 mm at the top
H=5200 mm
200
b= 3000 mm
tp= 750 mm
450

## Slide 21
Ph= ½ x 1/3 x 18 x 4.752=67.68 kN
M = Ph h/3 = 0.333 x 18 x 4.753/6
= 107.1 kN-m
Mu= 1.5 x M = 160.6 kN-m
Taking 1m length of wall,
Mu/bd2= 1.004 < 2.76, URS
(Here d=450- eff. Cover=450-50=400 mm)
To find steel
Pt=0.295% <0.96%
Ast= 0.295x1000x400/100 = 1180 mm2
#12 @ 90 < 300 mm and 3d ok
Ast provided= 1266 mm2 [0.32%]
Design of stem
Or Mu = [kaH3]/6
Pa
h
kah
M
Df

## Slide 22
Curtail 50% steel from top
(h1/h2)2 = 50%/100%=½
(h1/4.75)2 = ½, h1 = 3.36m
Actual point of cutoff
= 3.36-Ld=3.36-47 φbar = 3.36-0.564 = 2.74m from top.
Spacing of bars = 180 mm c/c < 300 mm and 3d ok
Curtailment of bars-Stem
Ast Provided
Ast/2
Ast
Dist.
from
top
h2
Every
alternate
bar cut
Ast
Ast/2
h2
Ldt
h1c
h1

## Slide 23
Development length (Stem steel)
Ld=47 φbar =47 x 12 = 564 mm
Secondary steel for stem at front
0.12% GA
= 0.12x450 x 1000/100 = 540 mm2
#10 @ 140 < 450 mm and 5d ok
Distribution steel
= 0.12% GA = 0.12x450 x 1000/100 = 540 mm2
#10 @ 140 < 450 mm and 5d ok
H=5200 mm
200
b= 3000 mm
tp= 750 mm
450

## Slide 24
Check for shear
Max. SF at Junction, xx = Ph=67.68 kN
Ultimate SF= Vu=1.5 x 67.68 = 101.52 kN
Nominal shear stress =ζv=Vu/bd
= 101.52 x 1000 / 1000x400 = 0.25 MPa
To find ζc: 100Ast/bd = 0.32%,
From IS:456-2000, ζc= 0.38 MPa
ζv < ζc, Hence safe in shear.
H=5200 mm
200
b= 3000 mm
x
x

## Slide 25: Stability analysis
Load | Magnitude, kN | Distance from A, m | BM about A kN-m
Stem W1 | 0.2x4.75x1x25 = 23.75 | 1.1 | 26.13
Stem W2 | ½ x0.25x4.75x1x25 = 14.84 | 0.75 + 2/3x0.25 =0.316 | 13.60
B. slab W3 | 3.0x0.45x1x25=33.75 | 1.5 | 50.63
Back fill, W4 | 1.8x4.75x1x18 = 153.9 | 2.1 | 323.20
Total | ΣW= 226.24 |  | ΣMR=413.55
Earth Pre. =PH | PH =0.333x18x5.22/2 | H/3 =5.2/3 | MO=140.05

## Slide 26
T
x1
x2
W1
W2
W3
W4
b/2
b/6
e
x
b
H/3
Pa
W
H
h
R
Pmax
Pmin.
0.75m
0.45m
1.8m
120.6
kN/m2
30.16
kN/m2
24.1
97.99
22.6
Pressure below the Retaining Wall
Forces acting on the wall and the pressure below the wall

## Slide 27: Stability checks
Check for overturning
FOS = ΣMR/ MO= 2.94 >1.55 safe
Check for Sliding
FOS = μ ΣW/ PH= 2.94 >1.55 safe
Check for subsidence
X=ΣM/ ΣW= 1.20 m > b/3 and e= b/2 –x = 3/2 – 1.2 = 0.3m < b/6
Pressure below the base slab
PMax=120.66 kN/m2 < SBC, safe
PMin = 30.16 kN/m2 > zero, No tension or separation, safe

## Slide 28: Design of heel slab
Load | Magnitude, kN | Distance from C, m | BM, MC, kN-m
Backfill | 153.9 | 0.9 | 138.51
Heel slab | 0.45x1.8x25 = 27.25 | 0.9 | 18.23
Pressure dist. rectangle | 30.16 x 1.8 =54.29 | 0.9 | -48.86
Pressure dist. Triangle | ½ x 24.1 x1.8=21.69 | 1/3x1.8 | -13.01
Total Load |  | Total | ΣMC=94.86
120.6 kN/m2
30.16 kN/m2
24.1
97.99
22.6
0.75m
0.45m
1.8m
Pressure below the Retaining Wall

## Slide 29: Design of heel slab-Contd.,
Mu= 1.5 x 94.86 =142.3 kNm
Mu/bd2= 0.89 < 2.76, URS
Pt=0.264% < 0.96%
Ast= 0.264x1000x400/100
=1056 mm2
#16@ 190 < 300 mm and 3d ok
Ast provided= 1058mm [0.27%]
OR Mu=0.87 fy Ast[d - (fyAst/fckb)]
H=5200 mm
200
b= 3000 mm
x
x

## Slide 30
Development length:
Ld=47 φbar
=47 x 16 = 752mm
Distribution steel
Same, #10 @ 140
< 450 mm and 5d ok
H=5200 mm
200
Ldt=752
x
x
Design of heel slab-Contd.,

## Slide 31: Design of heel slab-Contd.,
Check for shear at junction (Tension)
Maximum shear =V=105.17 kN,
VU,max= 157.76 kN,
Nominal shear stress =ζv=Vu/bd
= 101.52 x 1000 / 1000x400 = 0.39 MPa
To find ζc: 100Ast/bd = 0.27%,
From IS:456-2000, ζc= 0.37 MPa
ζv slightly greater than ζc,
Hence slightly unsafe in shear.
200
x
x

## Slide 32: Design of toe slab
Load | Magnitude, kN | Distance from C, m | Bending moment, MC, kN-m
Toe slab | 0.75x0.45x25 = | 0.75/2 | -3.164
Pressure distribution, rectangle | 97.99x0.75 | 0.75/2 | 27.60
Pressure distribution, triangle | ½ x22.6 x1.0.75 | 2/3x1=0.75 | 4.24
Total Load at junction |  | Total BM at junction | ΣM=28.67

## Slide 33: Design of toe slab
Mu= 1.5 x 28.67 =43 kN-m
Mu/bd2= 0.27< 2.76, URS
Pt=0.085% Very small, provide 0.12%GA
Ast= 540 mm2
#10 @ 140 < 300 mm and 3d ok
Development length:
Ld=47 φbar =47 x 10 = 470 mm
200
Ldt

## Slide 34: Design of toe slab-Contd.,
Check for shear: at d from junction (at xx as wall is in compression)
Net shear force at the section
V= (120.6+110.04)/2 x 0.35 -0.45x0.35x25=75.45kN
VU,max=75.45x1.5=113.18 kN
ζv =113.17x1000/(1000x400)=0.28 MPa
pt≤0.25%, From IS:456-2000, ζc= 0.37 MPa
ζv < ζc, Hence safe in shear.
200
x
x
d
Ldt
Notes: Net shear force at the section= (120.6+110.04)/2 x 0.35 -0.45x0.35x25=75.45kN
V=75.46 kN, VU,max=75.45x1.5=113.18 kN
τv=113.17x1000/(1000x400)=0.28 MPa
pt=0.25%
τuc =0.37 MPa
V,allowable = 0.37x 1000 x 400 =148 kN > VU,max, ok

## Slide 35: Other deatails
Construction joint
A key 200 mm wide x 50 mm deep
with nominal steel
#10 @ 250, 600 mm length in two rows
Drainage
100 mm dia. pipes as weep holes at 3m c/c at bottom
Also provide 200 mm gravel blanket at the back of the stem for back drain.

## Slide 36
L/S ELEVATION OF WALL
#16 @ 190
#12 @ 180
#12 @ 90
#10 @ 140
#10 @ 140
C/S OF WALL
Drawing and detailing

## Slide 37
PLAN OF BASE SLAB
BASE SLAB DETAILS
BOTTOM
STEEL
TOP
STEEL
Drawing and detailing